## Slide 1
Deep Dive INTO
EK-RA4E2
RENESAS Advanced MCU KIT
Ashish AHUJA
PRINCIPAL PRODUCT MANAGER & PRODUCT MARKETING MANAGER
RENESAS ADVANCED (RA) MCU KITS
Disclaimer
Renesas Electronics & its affiliates do not make any warranty of accuracy, usefulness, certainty or any other kind, relating to the contents & any other information in this presentation (hereinafter "Contents").The Contents including but not limited to physical & electrical specifications/characteristics of products, block diagrams, etc. are subject to change without any notice. In no event shall Renesas Electronics & its affiliates be liable for any loss, expense or damage arising out of or in connection with the use of or reliance upon the Contents. Please refer to the product datasheet & user manual for the most accurate information for the purpose of planning & developing your product.
All product & company names & logos are trademarks™ or registered® trademarks of their respective holders.
Picture: Queenstown | New Zealand

## Slide 2: AGENDA
Vision & Objective
of New RA Kits
Architecture
Features & Benefits
Deep Dive
Kit Features &
User Experience
Getting Started
Quickly

## Slide 3: VISION OF RA KITS
Deliver an unmatched innovation experience
through scalable, flexible & ecosystem-ready Renesas Advanced MCU kits that enable users to bring their innovative products to market faster.

## Slide 4: OBJECTIVE
To enable a large number of use cases so
customers, engineers, developers, distributors, partners, etc.
can do more
Functional Evaluation
Proof-of-Concepts
Getting Started Reference
Maker Community
Trainings & Workshops
Research & Academia
Solutions &
Demos
Promotions &
Lead Generation

## Slide 5: STRATEGY
Complexity of a MCU kit
Number of business enablement use-cases supported
Size of the circle => Number of MCU features supported by the kit
All MCU features
RA
Kits
Business
Serve global customer base
Facilitate cross-selling
Lower NRE & faster time to market
Technical
Useful for innovation
Support prioritized MCU peripherals
Ecosystem ready
User Experience
Delightful to use
Beautifully designed & presented
Typical Development Kit
Typical Starter Kit
Typical Breakout Board Kit
Biz.
Tech.
UX
RA
Kits

## Slide 6: DIFFERENTIATION that sets you apart
Innovation
Ready
A winning combination of standardization & flexibility
Ecosystem
Ready
Enhance functionality
on your terms
World
Ready
Compliant with many international standards
Fun
Ready
Take the guesswork out of your innovation experience

## Slide 7: KIT ARCHITECTURE
Ecosystem & System Control Access Area
Special Feature Access Area (optional)
MCU Native Pin Access Area
Power
Debug
Ecosystem expansion
Basic connectivity
User I/Os
Kit Information
High value functionality
MCU pins
MCU current measurement
Other MCU dependent functionality
Standard section
Flexible section
(MCU dependent)
Key Features of Architecture
Scalable design framework
Feature access organization
On-board access to most-popular ecosystems
Benefits of Architecture
Applicable across RA MCUs – new kits
Shorter learning curve for users
Improved user experience
Maximize hardware design reuse
Lower NRE
Faster time to market
Brings more innovation to users
Allows for vast functionality expansion
Fuels partner engagement and ecosystem utilization

## Slide 8: KIT ARCHITECTURE
Ecosystem & System Control Access Area
Special Feature Access Area (optional)
MCU Native Pin Access Area
Power
Debug
Ecosystem expansion
Basic connectivity
User I/Os
Kit Information
High value functionality
MCU pins
MCU current measurement
Other MCU dependent functionality
Standard section
Flexible section
(MCU dependent)
EK-RA6M4 Board
EK-RA4E2 Board
EK-RA2E1 Board
R7FA6M4AF3CFB

## Slide 9: KIT ARCHITECTURE
Ecosystem & System Control Access Area
Special Feature Access Area (optional)
MCU Native Pin Access Area
Power
Debug
Ecosystem expansion
Basic connectivity
User I/Os
Kit Information
High value functionality
MCU pins
MCU current measurement
Other MCU dependent functionality
Standard section
Flexible section
(MCU dependent)
Connect RA kits with ecosystem add-ons to enhance the functionality to support variety of end-applications

## Slide 10: THE WORLD OF INNOVATION AWAITS You!
EK-RA4E2
Evaluation Kit for RA4E2 MCU Group

## Slide 11: ECOSYSTEM & SYSTEM CONTROL ACCESS AREA
Front
Back
Power
Multiple power inputs
  USB debug
  USB full speed
  Clamping loops
  Through-hole points
On-board LDO 5 V to 3.3 V, 2 A
3.3 V test clamping loop
Power LED (white)
Superimpose currents by connecting multiple power sources simultaneously

## Slide 12: ECOSYSTEM & SYSTEM CONTROL ACCESS AREA
Front
Back
Debug & Trace
RA4M2 debug MCU
Segger J-LinkTM firmware
Debug connectors
  Micro USB (SWD)
  10-pin Cortex (SWD, JTAG)
  20-pin Cortex (SWD, JTAG, ETM)
Debug status LED (orange)
  Solid – debug drivers detected
  Blinking - debug drivers not detected
Debug modes selection jumpers

## Slide 13: MULTIPLE Debug MODES
External
Debugger
RA
Interface: SWD, ETM, JTAG
Connectors: 10-pin, 20-pin
Debug In
RA
RA4M2
Interface: SWD
Connectors: USB Debug, 10-pin, 20-pin
Debug Out
RA
Debug On-Board
Interface: SWD
Connector: USB Debug
RA4M2

## Slide 14: ECOSYSTEM & SYSTEM CONTROL ACCESS AREA
Front
Back
Ecosystem Expansion
2 SeeedGrove® system (I2C/Analog)
2 Digilent PmodTM (SPI & UART)
ArduinoTM (Uno R3)
MikroElektronikaTM mikroBUS
SparkFun® Qwiic®
User I/O
3x User LEDs (red, blue, green)
2x User buttons (blue)
Disconnect traces

## Slide 15: ECOSYSTEM & SYSTEM CONTROL ACCESS AREA
Front
Back
Serial Connectivity
SPI, I2C and UART through ecosystem headers
USB full speed (host & device)
  Micro AB connector
System Control
Reset button (red)
Boot configuration jumper
Others
Kit information area
  Version number
  Orderable part number
  Website

## Slide 16: SPECIAL FEATURES ACCESS AREA
Front
Back
High Speed Connectivity
CAN FD

## Slide 17: MCU NATIVE PIN ACCESS AREA
RA4E2
MCU
Front
Back
RA4E2 MCU
R7FA4E2B93CFM
MCU Breakout pins
1x 40-pin, 2x 14-pin male headers
3.3 V & ground available on each header

## Slide 18: MCU NATIVE PIN ACCESS AREA
Front
RA4E2 MCU
R7FA4E2B93CFM
MCU Breakout pins
1x 40-pin, 2x 14-pin male headers
3.3 V & ground available on each header
Enhanced prototyping support
Keyed to prevent incorrect insertion of custom daughter boards
Back
RA4E2
MCU

## Slide 19: MCU NATIVE PIN ACCESS AREA
RA4E2
MCU
Back
Front
RA4E2 MCU
R7FA4E2B93CFM
MCU Breakout pins
1x 40-pin, 2x 14-pin male headers
3.3 V & ground available on each header
Enhanced prototyping support
Keyed to prevent incorrect insertion of custom daughter boards
Current Measurement
MCU & USB current
Others
Clock generation & source selection
Reference voltage selection traces
RA4E2
MCU

## Slide 20: UX ENHACEMENTS
1. Practical & Aesthetic Layout & Placement
Design symmetry & segmentation
Connectors & button placement along the PCB edges for convenient access
Prototyping friendly break-out connector
Vertical & horizontal placement alignment
Clamping connectors – clamp, solder, contact
Simultaneous use of multiple features
  Except Arduino & MikroBUS connectors due to physical limitations
Front
Back

## Slide 21: UX ENHACEMENTS
1. Practical & Aesthetic Layout & Placement
Design symmetry & segmentation
Connectors & button placement along the PCB edges for convenient access
Prototyping friendly break-out connector
Vertical & horizontal placement alignment
Clamping connectors – clamp, solder, contact
Simultaneous use of multiple features
  Except Arduino & MikroBUS connectors due to physical limitations
2. “Using” & “Buying” Friendly Silk Screen
Consistent font type & size
Descriptive labeling
Vertical & horizontal text alignment & rotation
Help text – URLs, MCU & kit orderable part numbers, version number, compliance logos, serial number, etc.
Front
Back

## Slide 22: UX ENHACEMENTS
Tools Orderable Part Number (s) | Production Status | Manufacturer | Suggested Single Tool Price | Standard Packaging Quantity | Description | Distributor Stock | Distributors | Distributor Purchase
RTK7EKA2L1S00001BE | Mass Production | Renesas | call | 1 | Evaluation Kit for RA4E2 MCU Group | 5 | Future | Buy
 |  |  |  |  |  | 5 | Digi Key | Buy
 |  |  |  |  |  | 5 | Mouser | Buy
3. Website
renesas.com/ra/<kitname>
Easy to find collateral
Easy to order – live distributor stock
Consistently & professionally branded
High resolution pictures
4. Print Collateral
Consistently & professionally branded
Extensive & well-structured documentation
Consistent & intuitive file/folder nomenclature
  Kit name
  Document type
Easy to order
EK-RA4E2
Evaluation Kit for RA4E2 MCU Group
Product Info Design Support Documents Downloads Ordering
Title Issue Date Revision Doc Number Size (KB) Product Name
EK-RA4E2 – Quick Start Guide Rev.1.00 RXYZ1234567 2449 EK-RA4E2
EK-RA4E2 v1 – User’s Manual Rev.1.00 RXYZ987654 2450 EK-RA4E2
Quick Start Guide
Easy to find collateral
Intuitive & consistent file & folder nomenclature
ek-ra4e2-v1-designpackage
Design Files
Manufacturing Files
ek-ra4e2-v1-3d.pdf
ek-ra4e2-v1-bom.pdf
ek-ra4e2-v1-mechdwg.pdf
ek-ra4e2-v1-schematics.pdf
xxxxxxxx-cloud-connectivity-ek-ra4e2-ap
xxxxxxxx-cloud-connectivity-ek-ra4e2-ep
xxxxxxxx-cloud-connectivity-ek-ra4e2-an.pdf
xxxxxxxx-ek-ra4e2-qsg.pdf
xxxxxxxx-ek-ra4e2-v1-um.pdf
Consistently & professionally branded documentation
RA4E2 Group
Evaluation Kit for RA4E2 Microcontroller Group
EK-RA4E2 v1
User’s Manual
RA4 Series

## Slide 23: UX ENHACEMENTS
EK-RA4E2
Evaluation Kit for RA4E2 MCU Group
Product Info Design Support Documents Downloads Ordering
Title Issue Date Revision Doc Number Size (KB) Product Name
EK-RA4E2 – Quick Start Guide Rev.1.00 RXYZ1234567 2449 EK-RA4E2
EK-RA4E2 v1 – User’s Manual Rev.1.00 RXYZ987654 2450 EK-RA4E2
Quick Start Guide
5. Version Synchronization
Across All Version-specific Collateral
User’s manual
Kit board
Orderable part number
Packaging
Design package
  3D drawings
  BOM
  Mechanical drawings
  Schematics
Exclusions
  Quick start guide
Case-by-case exceptions
  Example projects
  Application notes
  Application projects
User’s manual
Kit version number & orderable part number
All version-specific collateral
Website
Packaging
ek-ra4e2-v1-designpackage
Design Files
Manufacturing Files
ek-ra4e2-v1-3d.pdf
ek-ra4e2-v1-bom.pdf
ek-ra4e2-v1-mechdwg.pdf
ek-ra4e2-v1-schematics.pdf
xxxxxxxx-cloud-connectivity-ek-ra4e2-ap
xxxxxxxx-cloud-connectivity-ek-ra4e2-ep
xxxxxxxx-cloud-connectivity-ek-ra4e2-an.pdf
xxxxxxxx-ek-ra4e2-qsg.pdf
xxxxxxxx-ek-ra4e2-v1-um.pdf
RA4E2 Group
Evaluation Kit for RA4E2 Microcontroller Group
EK-RA4E2 v1
User’s Manual
Renesas RA Family
RA4 Series

## Slide 24: WORLD READY
Certifications
EMC/EMI Standards
FCC Notice (Class A) – Part 15
Innovation, Science and Economic Development Canada ICES-003 Compliance: CAN ICES-3 (A)/NMB-3(A)
CE Class A (EMC Directive 2004/108/EEC)
Taiwan Chinese National Standard 13438, C6357 compliance, Class A limits
Australia/New Zealand AS/NZS CISPR 32:2015, Class A
Waste, Recycling and Material Selection
EU RoHS
China SJ/T 113642014, 10-year environmental protection use period
Safety Standards
UL 94V-0
User’s manual & quick start guide available in English & Japanese
RA4E2 Group
Evaluation Kit for RA4E2 Microcontroller Group
EK-RA4E2 v1
User’s Manual
Renesas RA Family
RA4 Series

## Slide 25: TOP NOTCH COLLATERAL (PPts, VIDEOS)
Click the thumbnails to view videos
Presentations and videos are available on renesas.com/ra/ek-ra4e2

## Slide 26: TOP NOTCH COLLATERAL (WEB, BLOGs)
EK-RA4E2 information and blogs are available on renesas.com/ra/ek-ra4e2
RA kit page renesas.com/ra/kits

## Slide 27: TOP NOTCH COLLATERAL - ENGINEERING
Design Package
Example Projects
All items are available on renesas.com/ra/ek-ra4e2
Quick start
guide
User’s manual
RA4E2 Group
Evaluation Kit for RA4E2 Microcontroller Group
EK-RA4E2
Quick Start Guide
Renesas RA Family
RA4 Series
RA4E2 Group
Evaluation Kit for RA4E2 Microcontroller Group
EK-RA4E2 v1
User’s Manual
Renesas RA Family
RA4 Series
Design &
manufacturing files
Schematics
Bill of Materials

## Slide 28: GETTING STARTED IS EASY!
Take the guesswork out of your innovation experience for an
unmatched, systematic & methodical approach to start developing
Watch the video
Click the image to watch the video

## Slide 29: GETTING STARTED IS EASY!
Choose your favorite kit
Order it from one of the leading global or regional distributors
Kit Name | Orderable Part Number | Kit Contents
EK-RA4E2 | RTK7EKA4E2S00001BE | EK-RA4E2 board, USB device, & USB host
1
Get your kit
2
Familiarize with your kit
3
Download & install software & tools
4
Explore & customize example projects
5
Expand functionality

## Slide 30: GETTING STARTED IS EASY!
Get quick start guide & user’s manual
Execute the Quick Start (QS) example project (EP) that is pre-programmed on the kit
Kit Name | Kit Homepage
EK-RA4E2 | renesas.com/ra/ek-ra4e2
1
Get your kit
2
Familiarize with your kit
3
Download & install software & tools
4
Explore & customize example projects
5
Expand functionality
Quick Start example project
Quick start guide & user’s manual
Welcome to Quick Start Example Project for EK-RA4E2!
> Select from the options in the menu below:
MENU
Kit Information
Next Steps
RA4E2 Group
Evaluation Kit for RA4E2 Microcontroller Group
EK-RA4E2
Quick Start Guide
Renesas RA Family
RA4 Series
RA4E2 Group
Evaluation Kit for RA4E2 Microcontroller Group
EK-RA4E2 v1
User’s Manual
Renesas RA Family
RA4 Series

## Slide 31: GETTING STARTED IS EASY!
1
Get your kit
2
Familiarize with your kit
3
Download & install software & tools
4
Explore & customize example projects
5
Expand functionality
Download & install software & tools using the FSP with e² studio installer that includes:
  Flexible Software Package – includes Hardware Abstraction Layer (HAL) drivers, Board Support Package (BSP), libraries, etc.
  e2 studio – Integrated Development Environment
  Need help anytime?
  Ask questions, get answers from experts & collaborate with community
  renesas.com/ra/forum
Item | Download page
FSP with e² studio installer | renesas.com/ra/fsp

## Slide 32: GETTING STARTED IS EASY!
Explore & customize Quick Start Example Project
  Visit EK-RA4E2 webpage renesas.com/ra/ek-ra4e2 and scroll down to “Documentation & Downloads” section
  Download EK-RA4E2 Example Project Bundle
  Extract the downloaded file xxxx-ek-ra4e2-exampleprojects.zip
  Browse to xxxx-ek-ra4e2-exampleprojects\ek_ra4e2\_quickstart\quickstart_ek_ra4e2_ep to locate the source code of the QS EP
  Refer to the quick start guide for instructions on modifying, rebuilding & programming the QS EP on your kit
Explore & customize additional Example Projects
  In the EK-RA4E2 Example Project Bundle downloaded in the step above, browse to xxxx-ek-ra4e2-exampleprojects\ek_ra4e2\ to locate the example projects provided for this kit
  Open xxxx-ek-ra4e2-exampleprojects.pdf to view the list of tool chain supported for each example project and additional reference documents
1
Get your kit
2
Familiarize with your kit
3
Download & install software & tools
4
Explore & customize example projects
5
Expand functionality

## Slide 33: GETTING STARTED IS EASY!
Choose from hundreds of add-on modules from the supported ecosystems to build custom proof-of-concept hardware
Choose from numerous software IPs from Renesas ecosystem partners for additional features
Refer to the kit design package to develop your custom board with feature enhancements
1
Get your kit
2
Familiarize with your kit
3
Download & install software & tools
4
Explore & customize example projects
5
Expand functionality
Design & manufacturing files
Schematics
BOM

## Slide 34: USEFUL RESOURCES
Ordering &
Documentation
User Manual, Design Package, Quick Start Guide
renesas.com/ra/ek-ra4e2
Example Projects
Access FSP and Example Projects for RA Kits
renesas.com/ra/KitEP
Video
Library
Learn more about RA MCU,
Kits, FSP, and Tools
renesas.com/ra/videos
Support
Community
Ask questions from experts
Collaborate with community
renesas.com/ra/forum
Feedback &
Feature Requests
Tell us how we are doing and how can enhance your experience
renesas.com/ra/KitFeedback

## Slide 35: BRING YOUR BIG IDEAS TO LIFE
Unmatched Innovation Experience
renesas.com/ra/kits

## Slide 36
renesas.com/ra/kits